## Slide 1
PSL Recognizer
Empowering Communication through AI
FYP-II Progress Presentation · Project Code: F25-115
Zain Baig (22K-4593) · Abdur Rehman (22K-4155) · Aarij Ali (22K-4264)
Supervisor: Miss Anum Qureshi · Co-Supervisor: Virkha Kumari
March 2026

## Slide 2
Agenda
01
Problem Statement & Motivation
02
Dataset & Signer-Disjoint Split
03
MediaPipe ROI Extraction Pipeline
04
Frame Pre-Extraction & Training Setup
05
Baseline: 3D-CNN + BiLSTM (from Scratch)
06
SignVLM: CLIP-Based Architecture
07
Results & Comparative Analysis
08
Why Scratch Failed / Why SignVLM Succeeded
09
Inference Pipeline & Next Steps

## Slide 3
Problem Statement & Motivation
Context
Pakistan's deaf community numbers over 1 million people, yet Pakistani Sign Language (PSL) remains severely underrepresented in automated recognition research.
No publicly available, signer-independent PSL recognition system exists.
FYP-I established a 104-class PSL dataset and a hybrid 3D-CNN + BiLSTM baseline — achieving 83.89% accuracy, but only under signer-inclusive evaluation.
FYP-II Objectives
1.
Establish signer-disjoint evaluation (true generalization)
2.
Apply MediaPipe hand ROI extraction to reduce noise
3.
Retrain 3D-CNN baseline under correct split
4.
Train SignVLM — CLIP-based low-resource architecture
5.
Develop real-time inference pipeline

## Slide 4
Dataset: Structure & Signer-Disjoint Splitting
104
PSL Classes
1,976
Total Videos
3
Signers
LOSO
Eval Protocol
Data Split
Split | Directory | Videos | Videos/Class
Training | train_data | 1,560 | ~15
Validation | validation_data | 312 | ~3
Test | test_data | 104 | 1 (exact)
Key Insight
FYP-I used random splits — signer videos leaked into test set, artificially inflating accuracy. FYP-II enforces strict signer-disjoint (LOSO) evaluation, mirroring real-world conditions where the model sees new signers it has never trained on.

## Slide 5
MediaPipe ROI Extraction Pipeline
Input Video
(.mp4 / .mov)
→
MediaPipe
Hand Detection
→
Bounding Box
+ Padding ×1.3
→
Bilateral Union
L + R Hands
→
Crop + Resize
to Fixed Res
→
Output ROI
Video (_roi.mp4)
Extraction Results — 100% Coverage
Split | Source Videos | ROI Generated | Coverage
Train | 1,560 | 1,560 | 100%
Validation | 312 | 312 | 100%
Test | 104 | 104 | 100%
Design Decisions
▸ Both hands merged into one crop (two-handed signs)
▸ Fallback: full frame when MediaPipe fails
▸ Extended to .mov files (iOS recordings)
▸ Padding factor 1.3× for full finger capture

## Slide 6
Frame Pre-Extraction for Efficient Training
The Bottleneck Problem
Real-time H.264 video decoding during training caused data_time to dominate — exceeding GPU compute by 5–10×. GPU utilization sat at only ~30%.
Unicode Path Problem (Windows)
OpenCV cv2.VideoCapture() silently fails on Urdu/Arabic class names (ب، آ، ے). All Urdu-class videos were silently skipped. Fixed using PyAV (FFmpeg bindings) with proper UTF-8 path handling.
Impact After Pre-Extraction
data_time
~0.8s/batch → ~0.05s/batch
16× faster
GPU Utilization
~30% → ~85–90%
+55 pts
Iter. Time
~5s/step → ~1.2s/step
4× faster

## Slide 7
Baseline: 3D-CNN + Residual Blocks + BiLSTM
Stage 1 — 3D-CNN Backbone
Input: (B, 3, T, H, W)
Conv3D(3→32) + BN + ReLU + Pool
Conv3D(32→64) + BN + ReLU + Pool
Conv3D(64→128) + BN + ReLU
2× ResidualBlock(128) + Pool
Output: (B, T', 128)
→
Stage 2 — BiLSTM
Input: (B, T', 128)
BiLSTM(128→256, 2 layers)
Bidirectional: captures both
forward & backward context
Last timestep → (B, 512)
Dropout(0.3)
→
Stage 3 — Classifier
Input: (B, 512)
Linear(512 → 104)
Softmax over 104 classes
~2.5M total parameters
Trained from scratch
Random initialization
Training Config: AdamW · Cosine LR Schedule · AMP (Mixed Precision) · Label Smoothing · Early Stopping · WeightedRandomSampler

## Slide 8
SignVLM: CLIP-Based Visual-Temporal Architecture
CLIP ViT-L/14
(Frozen Encoder)
Pretrained on 400M image-text pairs
14×14 patch grid · 1024-dim features
↓
EVL Temporal
Decoder
Lightweight temporal convolutions
Cross-frame attention · Parameter-efficient
↓
Softmax
Classifier
104-class output
Top-1 and Top-5 predictions
Why SignVLM for PSL?
Low-Resource Design
Designed explicitly for sign language tasks with limited training data
Rich Visual Priors
CLIP already understands hands — no need to learn from scratch
Signer Invariance
Text-image alignment naturally abstracts away identity-specific appearance
Proven Benchmarks
Outperforms RGB baselines on ASL, Arabic SL, LSA64, AUTSL

## Slide 9
Experimental Results & Comparative Analysis
2.88%
3D-CNN from Scratch
Top-1 (Signer-Disjoint)
60.26%
SignVLM
Top-1 (Signer-Disjoint)
71.15%
SignVLM
Top-5 (Signer-Disjoint)
83.89%
FYP-I 3D-CNN
Top-1 (Random Split)
Context: 104 classes · ~15 training clips/class · Evaluated on signers entirely unseen during training — a genuinely difficult low-resource benchmark.
Per-Class Finding
English-alphabet classes: ~70–80% accuracy · Urdu/Arabic classes: ~40–55%
CLIP's internet pretraining is better aligned with Western signing contexts — motivating targeted data collection for Urdu-script classes.

## Slide 10
Why Scratch Models Failed: Root Cause Analysis
01
Catastrophic Data Scarcity
~15 videos/class vs. 600+/class for Kinetics-400. Our dataset is 40× smaller than the minimum viable condition for from-scratch 3D-CNN training.
02
Inverted Parameter-to-Sample Ratio
~2.5M parameters · 1,560 training samples → ~1,600 params per example. Deep learning heuristics require ≥10 samples per parameter.
03
No Visual Priors for Hands
Without pretraining, the model must simultaneously learn what hands look like AND how their motion maps to signs — from 15 examples.
04
Signer-Disjoint Split Removes the Safety Net
FYP-I's random split let the model memorize signer-specific appearance. FYP-II's LOSO split removed this shortcut, revealing true representational capacity.

## Slide 11
Why SignVLM Succeeded: Transfer Learning from Scale
CLIP's Visual Prior Eliminates the Data Bottleneck
Pretrained on 400M image-text pairs. Immediately produces rich 1024-dim hand embeddings. The EVL decoder only learns temporal patterns from PSL data — not visual representation from scratch.
EVL Temporal Decoder is Parameter-Efficient
Lightweight temporal convolutions + cross-frame attention on top of a frozen backbone. Comparatively few new parameters — all trained from 1,560 samples without overfitting.
Pretrained Representations are Signer-Agnostic by Design
CLIP's image-text alignment objective produces identity-abstract features. A description like 'a hand making a gesture' applies regardless of who is signing it.
Validated on Multiple Benchmarks
SignVLM outperforms pure RGB pipelines on ASL, Arabic SL, LSA64, and AUTSL. The performance gap is largest in low-data settings — exactly our scenario with ~15 samples/class.

## Slide 12
Inference Pipeline & Real-Time Deployment
Webcam
(30 fps)
→
Sliding Window
Buffer (~2s)
→
MediaPipe
ROI Detection
→
Uniform Frame
Sampling (16)
→
CLIP ViT-L/14
Feature Extraction
→
EVL Temporal
Decoder
→
Top-1 Prediction
+ Confidence
RTX 3060 Performance
CLIP ViT-L/14 on 16 frames: ~40–60ms/clip
→ 15–25 recognition decisions per second with 2s sliding window — suitable for near-real-time feedback.
Confidence Thresholding
Raw predictions filtered at softmax threshold (e.g., 0.4). Below-threshold clips shown as 'uncertain' — reducing false positives in practical usage.
Next Steps
▸ Run test-set evaluation (checkpoint-5000.pth)
▸ Upgrade 3D-CNN to pretrained R3D-18 backbone (Kinetics-400)
▸ Evaluate SignVLM on ROI data vs. full-frame data
▸ Collect additional signer data (even 1–2 more signers)
▸ Implement real-time webcam demo with Gradio

## Slide 13
Summary
Signer-Disjoint Split:
LOSO evaluation reveals true generalization. FYP-I results inflated by signer leakage.
MediaPipe ROI Extraction:
100% coverage. Both-hand unified crop with fallback — stable pipeline for all 1,976 videos.
3D-CNN from Scratch:
2.88% accuracy on signer-disjoint test. Confirms literature: small datasets cannot train deep video models.
SignVLM (CLIP ViT-L/14):
60.26% Top-1 · 71.15% Top-5 — meaningful result on 104 classes with ~15 samples/class.
Transfer Learning is Essential:
CLIP's visual priors eliminate the data bottleneck and provide inherent signer invariance.
Thank You · Questions Welcome